## Slide 2: Chemkin database Parser
Manikandarajan.M
Kameshwaran.B.N

## Slide 3: Objective
Use an octave script file to read data from the Chemkin formatted database and find the thermodynamic properties of gases
Understand the behaviour of gases at various temperature – from the temperature curves

## Slide 4: Motivation
Octave is a new tool for us to use
Octave being a high level language is much simple to the user
Scientific computing along with intelligence of machine makes complex problems simple
Experimenting with newer concepts and algorithms is always fun

## Slide 5: Coding Framework
Locate the database
Look for the interested Gas (aka species)
Find the effective range of temperature
Get all the coefficients for that range of temperature
Calculate cp, Ho , So
Plot a curve for all properties vs. Temperature

## Slide 6
Coding Framework (contd...)
The equations are
cp = cal/mol-K R=1.987 cal/mol-K
Ho = cal/mol
So = cal/mol-K

## Slide 7
Coding Framework (contd...)
Understanding the database :
Line 1 : Species Name Tmin Tmax Tmid
Line 2 : Coefficients (a1 to a5 )
Line 3 : Coefficients (a6 to a10 )
Line 4 : Coefficients (a11 to a14 )
:: Coefficients are precise of 10 decimal points in scientific notation

## Slide 9
Script pseudocode:
LOAD database
INPUT Species, Temperature
FIND Species
IF FOUND
FIND Temperature limits for the input temperature
FIND coefficients in the successive lines
OTHERWISE
PRINT Not Found
CONVERT coefficients into numbers from string
CALCULATE cp , Ho , So

## Slide 10
Script Pseudo code (contd...)
PRINT cp, Ho , So
FOR Temperature = lower limit : upper limit
CALCULATE properties for all temperature
PLOT properties vs. Temperature
RELEASE the database

## Slide 11
Script file (explained)

## Slide 12
Using script
In Octave GUI :
In Octave CLI

## Slide 13
Plot Results
CH4

## Slide 14
Testing
The plots can be checked by molar mixing or mass mixing
  Cp of air = cp of N2 * 0.79 + cp of O2 * 0.21 (by molar mixing)
  Cp of air = cp of N2 * 0.77 + cp of O2 * 0.23 (by mass mixing)
eg., @ 300 K , cp of N2 = 6.948 and O2 = 7.023
Hence, for air = 6.948(0.79) + 7.023(0.23) = 7.104 cal/mol-k
In J/mol-k cp = 29.83

## Slide 15
Testing (contd...)
The air values can be referred from standard tables for different temperatures
Temperature out of bounds are input for any misbehavior of the output
Similarly, unknown species, species(case-sensitive) are also tested.

## Slide 16
Inference
From the plots, the thermo chemical behaviour of the gases are studied.
For example, ammonia gas has lowered heat capacity above 5000 K
H2 has lower enthalpy than H

## Slide 17
Comparison
CO2

## Slide 18
Comparison (contd...)
N

## Slide 19
Comparison (contd...)
NH3

## Slide 20
References:
http://www.edxengine.com
http://www.gnu.org/software/octave/doc/v4.0.0/ (software help)
http://combustion.berkeley.edu/gri_mech/
http://combustion.berkeley.edu/gri_mech/version30/files30/thermo30.dat
http://combustion.berkeley.edu/gri_mech/data/nasa_plnm.html (equations)
http://www3.nd.edu/~powers/ame.60636/kee2000.pdf (manual)